## Slide 1: Journal Club Oct. 22
付祥

## Slide 2: 文章主要内容
衡量量子指令集功效的方法
  研究指令集的信息密度(Byte数）
设计空间探索是研究ISA的重要方法
  RISC-like指令集（基准线）
  eQASM
  基于RISC-V
    QUASAR
    qV

## Slide 3: Background
high-level quantum program
A “CPU Host” compiles it the into a sequence of instructions
Quantum Control Processor (QCP) translates these instructions into commands
Commands trigger Arbitrary Waveform Generators (AWG).
AWG controls the execution of the Quantum Processing Unit (QPU).

## Slide 4: Contribution
Optimality criteria
  Minimize the number of instructions to represent the application
  gate diversity/gate density/distribution balance
Two extensions to RISC-V
  QUASAR, quantum vector (qV)
Summary about capability & limitation of ISAs

## Slide 5: ISA Design Requirements
Physical implementation
  of the quantum device, and the related control electronics
  To support at least the native QPU gates
    we expect only a small number of opcodes
  To address all qubits
  The QCP is required to maintain gate application timings
  To support basic control and data flow operations
    classical instructions are essential in a QISA
Quantum circuit structure

## Slide 6: ISA Design Requirements
Physical implementation
Quantum circuit structure
  Gate density per per single time stamp (ts)
  Gate diversity per ts (No. gate types)
  Distribution balance

## Slide 7: ISA Design Space - RISC-like ISA
  QPU_ADDR: the base address for QCP
CPU
QCP
QPU

## Slide 8: ISA Design Space -eQASM

## Slide 9: ISA Design Space - QUASAR
An extension to RISC-V, 32-bit
Four types of quantum instructions
  single-qubit gates
  two-qubit gates
  measurement
  timing control
Addressing
  9-bit immediate (512 qubits)
  32-bit mask + 4-bit immediate offset (do not fully understand it)

## Slide 10: ISA Design Space - Double Index Quantum Vector (qV)
Quantum circuits express both
  SIMD: same gate, multiple qubits
  MIMD: multiple gates, multiple qubits

## Slide 11: ISA Design Space - Double Index Quantum Vector (qV)
vqqi: two-register format with an op field
  each register: a vector of qubit indices
  op: the same operation applied on these two vectors of qubits
  vld, vld, vqqi
vqqg: three-register format
  two registers, each a vector of qubit indices
  third register: a list of quantum gates
  mask: nop in vreg3, or 0 bit in vreg 1
  Question: which quantum gate to which qubit(s) in vreg1 and/or vreg2?
  vld, vld, vld, vqqg
描述与代码不匹配

## Slide 12: Evaluation
Encoding efficiency (in Bytes)
Execution time
Benchmarks
  Synthetic circuits with different characteristics
    Gate density, gate diversity, distribution balance
  Algorithm: 32-qubit QFT + Grover operator
Processor characteristics: ICE
  32-bit, 5-stage

## Slide 13: Experiment Result 1
Hard to understand where these numbers are from

## Slide 14: Experiment Result 2

## Slide 15: Experiment Result 3

## Slide 16: Experiment Result 4
Limited consideration in
  Pipeline flushing
  Memory access miss
  Pipeline stall

## Slide 17: Author’s Summary